# SETTING INSTRUCTIONS FOR AMANO 3600 SERIES TIME CLOCKS

REMOVE COVER.

THE SETTING LEVER IS LOCATED BEHIND THE 2 ON THE FACE.

LIFT AND RELEASE THE LEVER TO CHANGE THE TIME MINUTE BY MINUTE.

TO SET THE TIME RAPIDLY, HOLD THE LEVER UP AND ROTATE THE GEAR CLOCKWISE WITH YOUR FINGER.

NEVER FORCE THE LEVER OR GEAR IF IT DOESN’T TURN FREELY.

NEVER MOVE THE HANDS ON THE CLOCK FACE.

WAIT APPROXIMATELY 10 SECONDS AFTER IT CHANGES MINUTES BEFORE SETTING THE TIME, THE GEAR SHOULD TURN EASILY.

THE DATE WHEEL MAY BE TURNED MANUALLY AND WILL MOVE FREELY IN ONE DIRECTION.

THE MONTH WHEEL IS HELD IN PLACE BY A LEVER ON THE LEFT SIDE.  GENTLY PRESS THE LEVER TO RELEASE AND ADJUST THE MONTH.  THE WHEEL MAY BE MOVED IN EITHER DIRECTION. ONCE THE PROPER MONTH IS SET, RELEASE THE LEVER SO THAT IT SITS IN THE GROOVE TO LOCK THE WHEEL IN PLACE.

IF YOU HAVE ANY QUESTIONS, PLEASE FEEL FREE TO CONTACT US.

(800) 925-4506

SUPPORT@COMPUMATICTIME.COM

HARVEY KIPNES